## Slide 1: DIGITAL Communication

## Slide 2: Outline
What is communication?
Analog to Digital Conversion (A/D)
Source Coding
Channel Encoding
Modulation Techniques

## Slide 3: What is Communication?
Communication is transferring data reliably from one point to another.
Data could be: voice, video, images etc…
Communication system
A system that allows transfer of information reliably between transmitter and receiver.

## Slide 4: Destination
Transmitter
Channel
Receiver
Block Diagram of a typical communication system
Information
Source

## Slide 5
Information Source
  The source of data
    Data could be: human voice, video etc..
  Data types:
    Discrete/Digital: Finite set of values
    Continuous/Analog : Infinite set of values
Transmitter
  Converts the source data into a suitable form for transmission through signal processing
  Data form depends on the channel

## Slide 6
Channel:
  The physical medium used to send the signal where the signal propagates till arriving to the destination.
  Physical Media (Channels):
    Wired : twisted pairs, coaxial cable, fiber optics
    Wireless: Air, vacuum and water
  Every physical channel operates on a certain limited range of frequencies , that is called the channel bandwidth.
  Physical channels have another important drawback which is the Noise.

## Slide 7
Receiver
  Reproducing the message in the received signal
    Example
      Speech signal at transmitter is converted into electromagnetic waves to travel over the channel.
      Once the electromagnetic waves are received properly, the receiver converts it back to a speech form.
  Information Sink
    The final stage/User

## Slide 8: Digital Communication System Block Diagram
Information Source
A / D Converter
Source Encoder
Channel Encoder
Modulator
Information
Sink
D / A
Converter
Source
Decoder
Channel
Decoder
Demodulator
Channel

## Slide 9
Information source
  Analog Data: Microphone, speech signal, image, video etc.
  Digital Data: keyboard, binary numbers etc.
Analog to Digital Converter (ADC)
  Sampling:
    Converting continuous time signal to a discrete time signal
  Quantization:
    Converting the amplitude of the analog signal to a digital value
  Coding:
    Assigning a binary code to each finite amplitude in the signal

## Slide 10
Source encoder
  Data Compression- carried out to convert the analog signal to digital form.
  Data Compaction – carried out to produce a new data code that represents digital data more efficiently.
  Data Encryption – Licensed user with the required key can only decode and receive the data.

## Slide 11
Channel encoder:
  Controls the noise, detects and corrects the errors that can occur in the transmitted data due to noise in the channel.
Modulator:
  Converts the digital data into analog signals at can be easily sent on the analog signals.
Demodulator:
  Removes the carrier signal and reverse the process of the Modulator

## Slide 12
Channel decoder:
  Detects and corrects the errors in the signal received from the channel
Source decoder:
  Decompression & Decryption of the data into its original form.
Digital to Analog Converter:
  Reverses the operation of the Analog to Digital Converter
  Needs techniques and knowledge about sampling, quantization, and coding methods.
Information Destination

## Slide 13: Advantages of Digital communication
Ease of regeneration
  Pulses “ 0 , 1”
  Easy to use repeaters
Noise immunity
  Better noise handling when using repeaters
  Digital circuits are less prone to interference and distortion
Ease of Transmission
  Low error rates
  Reliability
  Ease of measurement

## Slide 14: Advantages of Digital communication
Ease of multiplexing
  Transmitting several signals simultaneously
Use of modern technology
  Integrated Circuit
Ease of encryption
  Security and privacy guarantee
  Handles most of the encryption techniques

## Slide 15: Disadvantages
The major disadvantage of digital transmission is that it requires a greater transmission bandwidth or channel bandwidth to communicate the same information in digital format as compared to analog format.
Another disadvantage is the requirements of precise synchronization between the transmitter and the receiver.

## Slide 16: Analog Signal to a Discrete Signal (A/D) Conversion
Can be done through three basic steps:
Sampling
Quantization
Coding

## Slide 17: Sampling
Process of converting the continuous time signal to a discrete time signal.
Sampling is done by taking “Samples” at specific regular time intervals.
  V(t) is an analog signal
  V(nTs) is the sampled signal
    Ts = positive real number that represent the spacing of the sampling time
    n = sample number integer

## Slide 18: Sampling
Original Analog Signal
“Before Sampling”
Sampled Analog Signal
“After Sampling”

## Slide 19: Sampling
The closer the Ts value, the closer the sampled signal resemble the original signal. Sampling rate must be large enough to allow analog signals to be reconstructed accurately.
We lose some values of the original signal, the parts between each successive samples.

## Slide 20: Sampling Theorem
A bandlimited signal having no spectral components above fmax (Hz), can be determined uniquely by values sampled at uniform intervals of Ts seconds, where
An analog signal can be reconstructed from a sampled signal without any loss of information if and only if it is:
– Band limited signal
– The sampling frequency is at least twice the signal
bandwidth

## Slide 21: Quantization
Quantization is the process of constraining an input from a continuous or large set of values (such as the real numbers) to a discrete set (such as the integers).
Dynamic range of a signal
– The difference between the highest to lowest value the signal can takes.

## Slide 22: Quantization
In the Quantization process, the dynamic range of a signal is divided into L number of amplitude levels denoted by mk, where k = 1, 2, 3, .. L
L is an integer power of 2
  L = 2k
  K is the number of bits needed to represent the amplitude level.
For example:
If we divide the dynamic range into 8 levels,
  L = 8 = 23
We need 3 bits to represent each level.

## Slide 23: Quantization
Example:
– Suppose we have an analog signal with the values between 0 and 10. If we divide the signal into four levels. We have
m1 |  | [ 0, 2.5 ]
m2 |  | [ 2.5, 5 ]
m3 |  | [ 5 , 7.5]
m4 |  | [ 7.5, 10]

## Slide 24: Quantization
Original Analog Signal
Quantized Analog Signal

## Slide 25: Quantization
Original Discrete Signal
Quantized Discrete Signal

## Slide 26: Quantization
The more quantization levels taken, the smaller the error between the original and quantized signal.
Quantization step
The smaller the Δ, the smaller the error.

## Slide 27: Coding
Assigning a binary code to each quantization level.
For example, if we have quantized a signal into 16 levels, the coding process is done as the following:
Step | Code | Step | Code | Step | Code | Step | Code
0 | 0000 | 4 | 0100 | 8 | 1000 | 12 | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | 13 | 1101
2 | 0010 | 6 | 0110 | 10 | 1010 | 14 | 1110
3 | 0011 | 7 | 0111 | 11 | 1011 | 15 | 1111

## Slide 28: Coding
The binary codes are represented as pulses
  Pulse means 1
  No pulse means 0
After coding process, the signal is ready to be transmitted through the channel. And therefore, completing the A/D conversion of an analog signal.

## Slide 29: Transmission
After encoding the binary data, the data is now ready to be transmitted through the physical channel
In order to transmit the data in the physical channel we must convert the data back to an electrical signal
– Convert it back to an analog form
This process is called modulation

## Slide 30: Modulation
Modulation is the process of changing a parameter of a signal using another signal.
The most commonly used signal type is the sinusoidal signal that has the form of :
  V(t) = A sin ( wt + θ )
A : amplitude of the signal
w : radian frequency
θ : Phase shift

## Slide 31: Modulation
If the carrier signal amplitude changes in accordance with the message signal, then the process is called as amplitude modulation.
If the carrier signal frequency changes in accordance with the message signal, then this process is known as frequency modulation.

## Slide 32: Modulation Types - AM

## Slide 33: Modulation Types - FM, PAM

## Slide 34: Digital Data Transmission
There are two types of Digital Data Transmission:
  Base-Band data transmission
    Uses low frequency carrier signal to transmit the data
  Band-Pass data transmission
    Uses high frequency carrier signal to transmit the data

## Slide 35: Transmission
Transmission bandwidth: the transmission bandwidth of a communication system is the band of frequencies allowed for signal transmission, in another word it is the band of frequencies at which we are allowed to transmit the data.
Bit Rate: It is the number of bits transferred between devices per second. If each bit is represented by a pulse of width Tb then the bit rate is

## Slide 36: Example – Bit rate calculation
Suppose that we have a binary data source that generates bits. Each bit is represented by a pulse of width Tb = 0.1 ms.
Calculate the bit rate for the source.
Solution:
R
b
1
b
1
T 0.1 10 3
10000 bits/sec

## Slide 37: Baud rate (Symbol rate)
The number of symbols transmitted per second through the communication channel.
The symbol rate is related to the bit rate by the following equation:
Rb = bit rate
Rs = symbol rate
N = Number of bits per symbol

## Slide 38: Baud rate (Symbol rate)
We usually use symbols to transmit data when the transmission bandwidth is limited
For example, we need to transmit a data at high rate and the bit duration Tb is very small; to overcome this problem we take a group of more than one bit, say 2.
By transmitting symbols rather than bits we can reduce the spectrum of the transmitted signal.

## Slide 39: Example
A binary data source transmits binary data, the bit duration is 1µsec, Suppose we want to transmit symbols rather than bits, if each symbol is represented by four bits. what is the symbol rate?
Each bit is represented by a pulse of duration 1µs, hence the bit rate
R
b
1
1 10 6
1000000 bits/sec

## Slide 40
Therefore, the symbol rate will be
R
s
N
Rb 1000000
4
250000 symbols/sec

## Slide 41: Bandpass Data Transmission
In communication, we use modulation for several reasons in particular:
  To transmit the message signal through the communication channel efficiently.
  To transmit several signals at the same time over a communication link through the process of multiplexing or multiple access.
  To simplify the design of the electronic systems used to transmit the message.
  by using modulation we can easily transmit data with low loss.

## Slide 42: Bandpass Digital Transmission
Digital modulation is the process by which digital symbols are transformed into wave-forms that are compatible with the characteristics of the channel.
The following are the general steps used by the modulator to transmit data
  1. Accept incoming digital data
  2. Group the data into symbols
  3. Use these symbols to set or change the phase, frequency or amplitude of the reference carrier signal appropriately.

## Slide 43: Bandpass Modulation Techniques
Amplitude Shift Keying (ASK)
Phase Shift Keying (PSK)
Frequency Shift Keying (FSK)
Multilevel Signaling (Mary Modulation)
  Mary Amplitude Modulation
  Mary Phase Shift Keying (Mary PSK)
  Mary Frequency Shift Keying (Mary FSK)
Quadrature Amplitude Modulation (QAM)

## Slide 44: Amplitude Shift Keying (ASK)
In ASK the binary data modulates the amplitude of the carrier signal.

## Slide 45: Phase Shift Keying (PSK)
In PSK the binary data modulates the phase of the carrier signal.

## Slide 46: Frequency Shift Keying (FSK)
In FSK the binary data modulates the frequency of the carrier signal.