## Slide 1: Pressure measurement
PRESSURE MEASUREMENT
Pressure is the action of one force against another over, a surface. The pressure P of a force F distributed over an area A is defined as: [ P = F/A ] Units of pressure: standard: N/m2 (Pa-Pascal), Kpa (Kilo Pascal) 1Bar=100kpa

## Slide 2
SENSING ELEMENTS
The main types of sensing elements are •Bourdon tubes •diaphragms •bellows . The basic pressure of sensing element can be configured as a C-shaped Bourdon tube (A); a helical Bourdon tube (B); flat diaphragm (C); a convoluted diaphragm (D); a capsule (E); or a set of bellows (F).

## Slide 4: Pressure Measurements
Bellows
Bourdon Tube
BELLOWS •
Bellows sensor is an axially flexible, cylindrical enclosure with folded sides. When pressure is applied through an opening, the closed end extends axially. • Bellows elements can measure absolute pressure, gauge pressure, vacuum, or differential pressure.
BOURDON TUBE •
A Bourdon gauge uses a coiled tube, which, as it expands due to pressure increase causes a rotation of an arm connected to the tube. • bourdon are often used in harsh environments and high pressures, but can also be used for very low pressures; the response time however, is slower than the bellows or diaphragm. C-type bourdon psi Range as low as 0 - 15 psi up to 0-1500 Helical bourdon Range as low as 0 - 200 psi up to 0 – 6000 psi Spiral bourdon Range as low as 0-10 psi up to 0-100,000 psi.

## Slide 11
THANK YOU
Notes: THANK YOU