## Slide 1: HIGHWAY ENGINEERING

## Slide 2: CONTENTS
Introductions
Road Geometrics
Highway Surveys and plan
Road Material

## Slide 3: INTRODUCTION
Highway Engineering : - The branch of science or engineering which deals with the art of design , construction and maintenance of roads of different kinds is termed as Highway Engineering.
Modes Of Transportation
Railways
Waterways
Airways

## Slide 4: IMPORTANT TERMS USED IN HIGHWAY ENGINEERING
Road :- Road is defined as a structure as a constructed of different material to facilitate movement of vehicle, carts , cyclists, pedestrians etc. from on place to another.
Traffic :- The motor vehicles of different kinds such as carts, cyclists and pedestrians moving together on a road is termed as traffic .

## Slide 5
Right of way :- The privilege to use road by the traffic is termed as right of way .
Street :- A road in a built up area or town is termed as street.
Carriage way :- The part of road, which is used only by vehicular traffic i.e. bullock carts and motor vehicles etc. is known as carriage way.
Foot path :- The part of road used by pedestrians or general people walking on foot is termed as foot path.

## Slide 6: FUCTIONS OF IMPORTANT ORGANISTIONS PROMOTING ROAD DEVELOPMENT IN INDIA
INDIA ROAD CONGRESS (I.R.C) : As per the recommendations made by the Jayakar Committee, a semi-government body was formed in 1934 to provide a platform for regular sharing of ideas and experience on all matters related to planning, construction and maintenance of roads in India. The body was named as India Road Congress (I.R.C)

## Slide 7: Function of I.R.C :
To collect information and literature on roads and make it available for use in the country.
To recommend standard specifications for road materials, design and construction techniques.
To determine the nature and extent of research.
To channelise consulative service on road research.

## Slide 8
Central road research institute (C.R.R.I) :-
In 1950, C.R.R.I was set up at okhla near delhi situated on Delhi-Mathura road to carry out research on various aspects of road engineering. This institute inaugurated by late PM is financed and controlled by MOST and is one of the national laboratories of the Council of Scientific and Industrial Research . It may be indicated that like I.R.C., C.R.R.I. Was also set up on the recommendations of jayakar committee report as a central organization of information and research. The head of the institute is known as director. He is assisted by deputy director.

## Slide 9: Functions of C.R.R.I :
To carry out research on various aspects of Highway Engineering.
To provide technical advice to State Government and Industries on various problems concerning roads such as traffic problems.
To co-ordinate the activities of State Road Boards located at Kolkata , Chennai , Luck now and Patna.

## Slide 10: National Highway Authority Of India (NHAI) :
National Highway Authority Of India known as NHAI is an autonomous statutory organization which was established on 15th June ,1989 under National Highway Authority Of India Act 1988. It is working under guidance of Ministry of Surface Transport (MOST) and is responsible for development , maintenance and management of National Highways in India. Its head office is situated in New Delhi.

## Slide 11: Functions Of NHAI :
To develop , maintain , and manage National Highways in India.
To implement National Highway development projects sectioned by MOST.
To construct express ways.
To invite tender and award projects to various highway building companies.
To handle BOT projects(Build-Operate-Transfer).

## Slide 12: IRC CLASSIFICATION OF ROAD
NATIONAL HIGHWAY
STATE HIGHWAY OR PROVINCIAL HIGHWAYS
MAJOR DISTRICT ROAD
OTHER DISTRICT ROAD
VILLAGE ROAD

## Slide 13: ORGANISATION OF STATE HIGHWAY DEPARTMENT

## Slide 14: SCOPE OF HIGHWAY ENGINEERING :-
Development, planning and location.
Design of road geometrics
Road economics
Road specification
Road bridges and culvert
Road making materials
Road administrations

## Slide 15: ROAD GEOMETRICS
Various Elements Of Road Geometrics
Right of way
Formation width
Road margin
Road shoulder
Carriage Way
Side slopes
Kerbs
Horizontal and vertical
curve
Formation level
Camber
Gradient
Design and average running speed
Stopping and passing sight distances
Super elevation

## Slide 17: TYPES OF CURVES:
Horizontal Curves
Vertical Curves
Advantages of curves :
To provide comfort to the passengers using roads on change of direction or grade.
To alert the driver against any mishap due to change in the direction of road.
To keep the speed of vehicles within limits.

## Slide 18: SUPER ELEVATION:
The transverse inclination provided to the pavement surface on curves by raising the outer edge with respect to the inner edge to counter act the centrifugal force and to reduce the tendency of vehicle to overturn is termed as SUPER ELEVATION

## Slide 19: Methods of Super Elevation:
Outer slope rotation method
Diagonal curve method
ADVANTAGES OF SUPER ELEVATION:
The stability of fast moving vehicle is increased and their tendency to skid or overturn decreases.
The distribution of pressure on both the wheels will be equal and thus wear and tear of vehicle decreases.
Intensity of stresses on the foundation decreases.

## Slide 20: HIGHWAYS SURVEYS AND PLANS :
Highway survey or road survey and infact highway planning is essential for a new road project. Road project means planning, designing and construction of a new road connecting to terminal points or town with the existing road network. Road survey are generally under taken to collect the necessary data and to determine the location of a proposed road.

## Slide 21
Assessment of road length requirement in a village, district, state or entire country.
Preparation of master plan of entire road project.
The road project includes the following:
Preparation of Topographic map
Road alignment.
Estimates and
Project report

## Slide 22
TOPOGRAPHIC MAP
A Map Showing the general details of an area such as building, roads, railway lines, sources of water, hospitals, schools, drainage structure etc. including contour lines is termed as topographic map.
USES OF TOPOGRAPHIC MAP :-
It helps to mark all the possible alignment and suggest the likely routes of the new road.
It helps to finalize the road gradient.
It helps to locate the position of bridges on the river or stream.

## Slide 23: ROAD ALIGNMENT
The route along which the centre line of a road is located in the plan or on the ground is termed as road alignment.
Requirement of an ideal road alignment :-
The road alignment b/w two station should be as short and straight as possible.
The road alignment should be economical.
The road alignment should be safe for traffic operations.

## Slide 24: BASIC CONSIDERATION GOVERNING ALIGNMENT FOR A ROAD IN PLAIN AREA :-
Factors
1 Obligatory points
2 Traffic consideration
3 Geometric Design Parameters
4 Economic Factors

## Slide 25: STANDARDS FOR PREPARING HIGHWAY PLANS
1Preparation of highway plans
2 Master plan
3 Estimates
4 Project report

## Slide 26: ROAD MATERIALS
Road materials
1 Soil
2 Aggregates
3 Binders

## Slide 27: TESTING OF ROAD MATERIALS
1 SOILS …..
CBR Test
2 AGGREGATES…..
Los angels abrasion test
Impact test
Crushing strength test
Water absorption test
Sound test

## Slide 28
3 Binders
Penetration test
Ductility test
Softening point
viscosity test

## Slide 29
THANK YOU